## Slide 1: DOPA 31/08/2023 Review of DOPA indicators
Giacomo Delli

## Slide 2
Previous version:
Categorical data (30m spatial resolution)
  1 = water surface
  2 = land no built-up in any epoch
  3 = built-up from 2000 to 2014 epochs
  4 = built-up from 1990 to 2000 epochs
  5 = built-up from 1975 to 1990 epochs
  6 = built-up up to 1975 epoch
Reference years:
1975, 1990, 2000, 2014
Latest version (R2023A)
Continuous data (100m resolution, 1 pixel=1 ha)
  m2 of built up within the pixel (0 – 10000 m2 )
Reference years:
5-years intervals from 1975 to 2020 and projections for 2023 and 2030
GHSL - BUILT UP SURFACE

## Slide 3
Previous version:
Continuous data (9 arcsecs spatial resolution)
  number of people per cell
Reference years:
1975, 1990, 2000, 2014
Latest version (R2023A)
Continuous data (3 arcsecs spatial resolution)
  number of people per cell
Reference years:
5-years intervals from 1975 to 2020 and projections for 2023 and 2030
GHSL - POPULATION
Sea Surface Temperature (monthly averages):
Copernicus Marine Data Store do not provide anymore the relevant dataset used for this indicator.
  - It could be computed starting from daily data (> 200Gb of data to be downloaded and processed) or
  - The SST metric will remain stuck to the temporal extent 2007 – 2019

## Slide 4
Continuous data (%, 0 - 100)
Temporal series from 2003 to 2020
1. The metric has to be defined. Alternative options:
  Mean O.P. computed on the last available year
  Net change 2003-2020
  Trend over the whole time series?
2. The Factsheet has to be developed​
Ocean Productivity index available to Fish (OPFish)